## Slide 1: Eat pizza – drink brus we will start ~17:45
pick up your kits before that (and pay for the training)

## Slide 2: (AVR) Microcontroller Basics
28.03.2022
Egil Rotevatn with Snorre Vestli, Amund Aune and Runar Sivertsen
Notes: Does anyone want me to do today’s presentation in English? Let me know

## Slide 3: µBedpress
  High-performance standard and specialized Microcontrollers, Digital Signal Controllers and Microprocessors
  Mixed-Signal, Analog, Interface and Security solutions
  Clock and Timing solutions
  Wireless and Wired Connectivity solutions
  FPGA solutions
  Non-volatile EEPROM and Flash Memory solutions
  Flash IP solutions
Leading Total Systems Solutions Provider:
~18,000
Employees
Headquartered near Phoenix in Chandler, AZ
$5.3 Billion Revenue FY2020

## Slide 4: µBedpress
Wireless
Wi-Fi®
Bluetooth®
LoRa®
802.15.4
zigbee® /MiWi™
Power
Drivers
Motor
Drivers
Encryption
&
Security
LED
Drivers
Amplifiers
Sensors
Filters
A/D
D/A
Precision
Voltage
Reference
Auto/Industrial
Communication
MOST®
Ethernet
INICnetTM
RS232/485
CAN/LIN
DC-DC Converters
Supervisors & Ref.
LDOs, Battery Mgt.
Discretes & Modules
Power Management
High Voltage
I/Os
Memory
EEPROM
Serial Flash
Serial SRAM
Serial EERAM
RFICs
MMICs
USB
Smart Hubs
Switches
Transceivers
Bridges
Smoke Detector
& Piezoelectric
Horn Drivers
Timing
Oscillators
Clock Generators
Clock Buffers
Network Synch.
Microcontrollers
Microprocessors
FPGA/ SoCs
Ethernet
Switches
Controllers
EtherCAT®
PHYs
PoE
Touch Sensing
Proximity/3D
Buttons/Slider
Touch Screen
Optical
Networking
Storage
PCIe® Switches
Adapters
Controllers
Voice &
Audio
Processing
Digital
Potentiometer

## Slide 5: µBedpress
Lausanne, Switzerland
Budapest, Hungary
Bucharest, Romania
Bangalore & Chennai, India
Brisbane, Australia
Shanghai, China
Hsinchu, Taiwan
Manila, Philippines
Bangkok, Thailand
San Jose , CA
Chandler, AZ
Norristown, PA
Hauppauge, NY
Austin, TX
Heilbronn & Karlsruhe, Germany
Gothenburg, Sweden
Nantes & Rousset. France
Ho Chi Minh City, Vietnam
Whiteley, UK
Penang, Malaysia
Trondheim, Norway
Irvine/San Diego, CA
Zaragoza, Spain
Shenzhen, China
Burnaby, Canada
Saskatoon, Canada
Calgary, Canada
Montreal, Canada
Ottawa, Canada
Toronto, Canada

## Slide 6: µBedpress
Microchip Technology Norway AS
  ~130 employees
  Located at Lyngården, Moholt
  Design, Test, Tools, Applications, Marketing
    8-bit Microcontrollers – AVR
    Human-Machine Interface – maXTouch
    Tools, Microchip Studio, MPLAB X IDE, Code composers

## Slide 7: Microchip 2.0
Be The Very Best Embedded Control Solutions Company Ever

## Slide 8: Annual Net Sales Growth
End Market Demand
Chart: 
| FY93 | FY94 | FY95 | FY96 | FY97 | FY98 | FY99 | FY00 | FY01 | FY02 | FY03 | FY04 | FY05 | FY06 | FY07 | FY08 | FY09 | FY10 | FY11 | FY12 | FY13 | FY14 | FY15 | FY16 | FY17 | FY18 | FY19 | FY20 | FY21 RR
MCU | 32.3 | 57.7 | 122 | 167.4 | 219.6 | 271.8 | 306.3 | 392.8 | 469 | 443.2 | 517 | 557 | 675 | 736 | 834 | 833 | 731.65 | 767.723 | 1013.937 | 928.509 | 1043.73 | 1260.988 | 1404.708 | 1345.499 | 2228.685 | 2619.099 | 3011.037 | 2883.679 | 2815.178
Analog | 70 | 42.5 | 47 | 51 | 57 | 66 | 83 | 83 | 82.3 | 99.848 | 177.994 | 171.165 | 324.255 | 428.088 | 503.517 | 635.956 | 898.43 | 951.982 | 1567.247 | 1509.109 | 1438.882
FPGA | 326.051 | 377.358 | 371.022
LMO | 56.4 | 81 | 86 | 118.5 | 114.7 | 125.1 | 100.2 | 101.1 | 177 | 85.4 | 87 | 92 | 115 | 125 | 123 | 120 | 89.34 | 80.158 | 295.274 | 283.502 | 238.386 | 242.141 | 252.381 | 232.38 | 374.573 | 409.684 | 568.826 | 572.178 | 536.292
$ Million
120 consecutive quarters of profitability!

## Slide 9: Worldwide 8-Bit Microcontroller Market Share
No. | 1991 Rank | 1996 Rank | 2001 Rank | 2005 Rank | 2006-2009 Rank | 2010 Rank | 2014-2017 Rank | 2017-2020 Rank
1 | Motorola | Motorola | Motorola | Motorola | Microchip | Renesas | Microchip | Microchip
2 | Intel | NEC | Hitachi | Renesas | NEC | Microchip | NXP | NXP
3 | Philips | Philips | NEC | Microchip | STMicro | Atmel | Renesas | Renesas
4 | Mitsubishi | Hitachi | Microchip | NEC | Freescale | STMicro | STMicro | STMicro
5 | NEC | Mitsubishi | STMicro | STMicro | Atmel | Samsung | CEC Huada | Others
6 | Hitachi | Toshiba | Philips | Atmel | Renesas | Freescale | Cypress | 
7 | Toshiba | Matsushita | Toshiba | Toshiba | NXP | NXP | Si Labs | 
8 | Siemens | SGS-Thomson | Atmel | Philips | Cypress | Cypress | Datang | 
9 | TI | Intel | Matsushita | Fujitsu | Sony | Panasonic | SH Fudan | 
10 | Matsushita | Microchip | Sanyo | Infineon | Fujitsu | Fujitsu | Holtek | 
11 | National | Siemens | Samsung | Sanyo | Panasonic | Detang | Unigroup | 
12 | SGS-Thomson | Fujitsu | Mitsubishi | Samsung | Toshiba | NEC (1Q) | Panasonic | 
13 | Ricoh | TI | Infineon | Matsushita | Samsung | Sony | Nationz | 
14 | MHS | Sony | Sony | Sony | Datang | Toshiba | ABOV | 
15 | IIT | Zilog | TI | Sunplus | SI Labs | SI Labs | Ixys | 
16 | Sharp | Sharp | Fujitsu | Micronas | Holtek | JSC | Toshiba | 
17 | Fujitsu | Temic | Sunplus | Novatek | Infineon | Holtek | Sony | 
18 | Oki | Sanyo | Zilong | Intel | Elan | Infineon | On Semi | 
19 | Zilog | National | Novatek | Holtek | Winbond | Sonix | Sonix | 
20 | Sony | Oki | Micronas | Winbond | Denso | Elan | HZ Silan | 
23 | Microchip |  |  |  |  |  |  | 
Based on dollar shipment volume 1991-2020, Source: Gartner and Microchip
9

## Slide 10: Worldwide Microcontroller Market Share
No. | 1991 Rank | 1996 Rank | 2003 Rank | 2008 Rank | 2009 Rank | 2014 Rank | 2019 Rank | 2020 Rank
1 | Motorola | Motorola | Renesas | Renesas | Renesas | Renesas | Renesas | Renesas
2 | Intel | NEC | Motorola | NEC | NEC | Freescale | NXP | NXP
3 | Philips | Philips | NEC | Freescale | Freescale | ST-Micro | Microchip | Microchip
4 | Mitsubishi | Hitachi | Matsushita | Infineon | Samsung | Microchip | ST-Micro | ST-Micro
5 | NEC | Mitsubishi | Infineon | Samsung | Microchip | NXP | Infineon | Infineon
6 | Hitachi | Toshiba | Fujitsu | Microchip | TI | TI | TI | TI
7 | Toshiba | Matsushita | Toshiba | ST-Micro | Infineon | Infineon | Others | Others
8 | Siemens | SGS-Thom | Microchip | TI | St-Micro | Atmel |  | 
9 | TI | Intel | Samsung | Fujitsu | Fujitsu | Spansion |  | 
10 | Matsushita | Microchip | ST-Micro | NXP | NXP | Samsung |  | 
23 | Microchip |  |  |  |  |  |  | 
1991 &1996 data extrapolated from 8-bit MCU: Source: Gartner and Microchip
7.5%
9.0%
3.6%
10

## Slide 11: Analog & Interface Products
Smoke Detector ICs
Piezoelectric Horn Drivers
SAFETY AND SECURITY
ULTRASOUND
Amplifiers
Comparators
LINEAR
A/D Converters
DACs & Digital Potentiometers
MIXED SIGNAL
Power Monitoring & Metering
Current/DC Power
Measurement ICs
DC/DC Converters
System Supervisors
Voltage Detectors
Power MOSFET Drivers
Battery Chargers
POWER MANAGEMENT
PWM Controllers
Power Switches
Power MOSFETs
Display/LED Drivers
INTERFACE
CAN, CAN FD, LIN
USB and I/O Expanders
Ethernet
Wireless
Real-Time Clock/Calendar
HV Interface
Fan Control & Management
THERMAL MANAGEMENT
Temperature Sensors
Voltage References
Motor Drivers
Ultrasound Products
Power Modules
Oscillators
CLOCK AND TIMING
DDR & SCSI Terminators
Hot Swap Power Controllers
High-Speed Data/Video
Clock Generators
Clock Buffers
Network Synchronization

## Slide 12: Industrial
28% of Sales

## Slide 13: Automotive
15% of Sales

## Slide 14: Consumer
13% of Sales

## Slide 15: Communications
14% of Sales

## Slide 16: Computing
18% of Sales

## Slide 17: Defense and Aerospace
12% of Sales

## Slide 18: Microcontroller
The basics

## Slide 19: Basic Parts
A microcontroller must have
  A CPU
  Memory
  I/O controller
CPU
Memory
I/O Controller

## Slide 20: The CPU
This is what executes your program
Can do math
Can make decisions based on input
Runs the code stored in memory
if (mentor == smart){
printf(“Of course!”);
} else
{
printf(“Lies!”);
}
CPU
Memory
I/O Controller

## Slide 21: Memory
Stores the program
  Read and executed by the CPU
Stores temporary data
  Variables are saved here
Stores static data
  Not deleted when device is turned off
CPU
Memory
I/O Controller

## Slide 22: I/O Controller
CPU
Memory
I/O Controller
Pins are used to communicate with the outside world
Controls input/output pins
  Can set pin high or low
  Can read if pin is pulled high or low
  High = VDD = input voltage
  Low = GND = 0V
Some pins can output or read any voltage

## Slide 23: Microcontroller
It’s that easy!
…Okay, not quite.
Microcontrollers normally have more stuff
  Called Peripherals
  Vary from type to type
  Explained in the Data Sheet
CPU
Memory
I/O Control

## Slide 24: C
AVR microcontrollers are programmed in C
  Or Assembly for those who like a challenge
  Or other languages someone added support for
C is a hardware-near programming language from the 1970s
Each statement must end with a semicolon;
The program always starts in the main() function
Must be compiled for the AVR architecture

## Slide 25: C
#define F_CPU 3333333UL
#include <avr/io.h>
#include <util/delay.h>
#define LED0PORT PORTF
#define LED0_bp PIN5_bp
int main(void)
{
LED0PORT.DIR |= (1 << LED0_bp);
while (1)
{
LED0PORT.OUT ^= (1 << LED0_bp);
_delay_ms(500);
}
}

## Slide 26: Bits & Bytes
1 bit = 0 or 1
8 bits == 1 byte
Representation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Sum
Binary | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0b11111111
Decimal | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 255
Hexadecimal | F |  |  |  | F |  |  |  | 0xFF

## Slide 27: Bits & Bytes
Bitwise OR: (A ¦ B) |  |  |  |  |  |  |  |  |  |  |  | 
Truth table: |  |  |  | Example: |  |  |  |  |  |  |  | 
Input |  | Output |  |  | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0
0 | 0 | 0 |  | Input A | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 1 |  | Input B | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 1 |  | Output | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 |  |  |  |  |  |  |  |  |  | 
Bitwise AND: (A & B) |  |  |  |  |  |  |  |  |  |  |  | 
Truth table: |  |  |  | Example: |  |  |  |  |  |  |  | 
Input |  | Output |  |  | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0
0 | 0 | 0 |  | Input A | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 |  | Input B | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 |  | Output | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 |  |  |  |  |  |  |  |  |  | 

## Slide 28: Bits & Bytes
Bitwise NOT: (~A) |  |  |  |  |  |  |  |  |  |  |  | 
Truth table: |  |  |  | Example: |  |  |  |  |  |  |  | 
Input | Output |  |  |  | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0
0 | 1 |  |  | Input A | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
1 | 0 |  |  | Output | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1
Bitwise XOR: (A ^ B) - Exclusive OR |  |  |  |  |  |  |  |  |  |  |  | 
Truth table: |  |  |  | Example: |  |  |  |  |  |  |  | 
Input |  | Output |  |  | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0
0 | 0 | 0 |  | Input A | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 |  | Input B | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 |  | Output | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 |  |  |  |  |  |  |  |  |  | 

## Slide 29: Bits & Bytes
Left shifting: Multiply with 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 3
Left shift 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shifting: Divide by 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 160
Right shift 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 30: Bits & Bytes
Left shifting: Multiply with 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 3
Left shift 1 |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |  |  | 6
Left shift 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shifting: Divide by 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 160
Right shift 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 31: Bits & Bytes
Left shifting: Multiply with 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 3
Left shift 1 |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |  |  | 6
Left shift 2 |  |  | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |  |  | 12
Left shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shifting: Divide by 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 160
Right shift 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 32: Bits & Bytes
Left shifting: Multiply with 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 3
Left shift 1 |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |  |  | 6
Left shift 2 |  |  | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |  |  | 12
Left shift 3 |  |  | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |  |  | 24
Left shift 4 |  |  | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  |  | 48
Left shift 5 |  |  | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 96
Left shift 6 |  |  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 192
Left shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Left shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shifting: Divide by 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 160
Right shift 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 33: Bits & Bytes
Left shifting: Multiply with 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 3
Left shift 1 |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |  |  | 6
Left shift 2 |  |  | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |  |  | 12
Left shift 3 |  |  | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |  |  | 24
Left shift 4 |  |  | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  |  | 48
Left shift 5 |  |  | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 96
Left shift 6 |  |  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 192
Left shift 7 |  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 128
Left shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shifting: Divide by 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 160
Right shift 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 34: Bits & Bytes
Left shifting: Multiply with 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 3
Left shift 1 |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |  |  | 6
Left shift 2 |  |  | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |  |  | 12
Left shift 3 |  |  | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |  |  | 24
Left shift 4 |  |  | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  |  | 48
Left shift 5 |  |  | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 96
Left shift 6 |  |  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 192
Left shift 7 |  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 128
Left shift 8 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 0
Right shifting: Divide by 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 160
Right shift 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 3 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 4 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 5 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 6 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 7 |  |  |  |  |  |  |  |  |  |  |  |  | 
Right shift 8 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 35: Bits & Bytes
Left shifting: Multiply with 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 3
Left shift 1 |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |  |  | 6
Left shift 2 |  |  | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |  |  | 12
Left shift 3 |  |  | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |  |  | 24
Left shift 4 |  |  | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  |  | 48
Left shift 5 |  |  | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 96
Left shift 6 |  |  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 192
Left shift 7 |  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 128
Left shift 8 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 0
Right shifting: Divide by 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
Start value |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 160
Right shift 1 |  |  | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 |  |  | 80
Right shift 2 |  |  | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 |  |  | 40
Right shift 3 |  |  | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |  |  | 20
Right shift 4 |  |  | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 |  |  | 10
Right shift 5 |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |  |  | 5
Right shift 6 |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |  | 2
Right shift 7 |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1
Right shift 8 |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 36: Bits & Bytes
Left shifting: Multiply with 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
(A << 0) |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 |  |  | 3
(A << 1) |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 |  |  | 6
(A << 2) |  |  | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 |  |  | 12
(A << 3) |  |  | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 |  |  | 24
(A << 4) |  |  | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 |  |  | 48
(A << 5) |  |  | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 96
(A << 6) |  |  | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 192
(A << 7) |  |  | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 128
(A << 8) |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 0
Right shifting: Divide by 2n |  |  |  |  |  |  |  |  |  |  |  |  | 
Operation | bit 9 | bit 8 | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | bit -1 | bit -2 | Decimal
(A >> 0) |  |  | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 |  |  | 160
(A >> 1) |  |  | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 |  |  | 80
(A >> 2) |  |  | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 |  |  | 40
(A >> 3) |  |  | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 |  |  | 20
(A >> 4) |  |  | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0 |  |  | 10
(A >> 5) |  |  | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 |  |  | 5
(A >> 6) |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |  |  | 2
(A >> 7) |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 |  |  | 1
(A >> 8) |  |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  | 0

## Slide 37: Bitmask
A defined left-shifted bit or bits
Think bit positions, not values
  (1 << 3) is read as «Write ‘1’ to bit 3»
  You configure a bit, not writing a number
Bitmasks can be combined
  (1 << 3) | (1 << 6)
  is «Write ‘1’ to bits 3 and 6»
Zero-indexed
  (1 << 0) the first bit is bit 0.

## Slide 38: Bits & Bytes
Logical operators != bitwise operators
Logical NOT: (!A) |  |  |  | Logical OR: (A ¦¦ B) |  |  |  | Logical AND: (A && B) |  | 
Truth table: |  |  |  | Truth table: |  |  |  | Truth table: |  | 
Input |  | Output |  | Input |  | Output |  | Input |  | Output
0 |  | 1 |  | 0 | 0 | 0 |  | 0 | 0 | 0
<0 |  | 0 |  | 0 | ≠0 | 1 |  | 0 | ≠0 | 0
>0 |  | 0 |  | ≠0 | 0 | 1 |  | ≠0 | 0 | 0
 |  |  |  | ≠0 | ≠0 | 1 |  | ≠0 | ≠0 | 1

## Slide 39: Bits & Bytes
Logical operators != bitwise operators
Relational operators
0 == «False» 1 == «True»
Operator | Meaning of Operator | Example
== | Equal to | 5 == 3 evaluates to 0
> | Greater than | 5 > 3 evaluates to 1
< | Less than | 5 < 3 evaluates to 0
!= | Not equal to | 5 != 3 evaluates to 1
>= | Greater than or equal to | 5 >= 3 evaluates to 1
<= | Less than or equal to | 5 <= 3 evaluates to 0

## Slide 40: Bit-fu 1st Dan
Syntax | Operation
A + B | Add A and B
A - B | Substract B from A
A / B | Divide A by B
A * B | Multiply A with B
~A | Bitwise NOT
A & B | Bitwise AND
A ¦ B | Bitwise OR
A ^ B | Bitwise XOR
A >> n | Right shift A bitwise n bits
A << n | Left shift A bitwise n bits
A ¦¦ B | Logical OR
A && B | Logical AND
!A | Logical NOT
A == B | Equal to
A > B | Greater than
A < B | Less than
A != B | Not equal to
A >= B | Greater than or equal to
A <= B | Less than or equal to

## Slide 41: Pause? – 10 min?

## Slide 42: Registers
Special location in RAM
Full of bits linked to module functions
Explained in data sheet and manual

## Slide 43: Registers

## Slide 44: Registers
Header file contains definitions and names
  #include <avr/io.h>
/* I/O Ports */
typedef struct PORT_struct
{
register8_t DIR; /* Data Direction */
register8_t DIRSET; /* Data Direction Set */
register8_t DIRCLR; /* Data Direction Clear */
register8_t DIRTGL; /* Data Direction Toggle */
register8_t OUT; /* Output Value */
register8_t OUTSET; /* Output Value Set */
register8_t OUTCLR; /* Output Value Clear */
register8_t OUTTGL; /* Output Value Toggle */
register8_t IN; /* Input Value */
register8_t INTFLAGS; /* Interrupt Flags */
register8_t PORTCTRL; /* Port Control */
...
} PORT_t;
#define PORTA (*(PORT_t *) 0x0400) /* I/O Ports */
Notes: Fancy variables located at special memory location

## Slide 45: Registers
PORTA.DIR = 0xff; // Set all PORTA pins as output
PORTA.OUT = 0; // Set all PORTA pins low
PORTA.OUT = 12; // You can do this, but only if you want to annoy people
// Better to do it like this: PORTA.OUT = (1 << PIN3_bp) | (1 << PIN2_bp); // Set pins PA2 and PA3 high
PORTA.PIN1CTRL = (1 << PORT_INVEN_bp); // Invert pin functionality of PA1

## Slide 46: Registers
Think bit positions, not values
  You configure bits, not writing a number
Bad examples:
Good examples:
        PORTA.OUT = 8;
        PORTA.OUT = 0b00001000;
        PORTA.OUT = (1 << 3);
        PORTA.OUT = (1 << PIN3_bp);
Notes: Callback to bitshifting

## Slide 47: Bits & Registers
Normal write to register: (A = B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0xE0
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A |  |  |  |  |  |  |  |  | 
Set bit(s) in register: (A ¦= B), long form: (A = A ¦ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A |  |  |  |  |  |  |  |  | 
New value B |  |  |  |  |  |  |  |  | 
Updated register A |  |  |  |  |  |  |  |  | 

## Slide 48: Bits & Registers
Normal write to register: (A = B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | x | x | x | x | x | x | x | x | 
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Set bit(s) in register: (A ¦= B), long form: (A = A ¦ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A |  |  |  |  |  |  |  |  | 
New value B |  |  |  |  |  |  |  |  | 
Updated register A |  |  |  |  |  |  |  |  | 

## Slide 49: Bits & Registers
Normal write to register: (A = B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | x | x | x | x | x | x | x | x | 
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Set bit(s) in register: (A ¦= B), long form: (A = A ¦ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A |  |  |  |  |  |  |  |  | 

## Slide 50: Bits & Registers
Normal write to register: (A = B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | x | x | x | x | x | x | x | x | 
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Set bit(s) in register: (A ¦= B), long form: (A = A ¦ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A | x | x | 1 | x | x | x | 1 | x | 

## Slide 51: Bits & Registers
Normal write to register: (A = B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | x | x | x | x | x | x | x | x | 
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Set bit(s) in register: (A ¦= B), long form: (A = A ¦ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A | 1 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0xA7

## Slide 52: Bits & Registers
Clear bit(s) in register: (A &= ~B), long form: (A = A & ~B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Inverted value B |  |  |  |  |  |  |  |  | 
Updated register A |  |  |  |  |  |  |  |  | 
Toggle bit(s) in register: (A ^= B), long form: (A = A ^ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A |  |  |  |  |  |  |  |  | 
New value B |  |  |  |  |  |  |  |  | 
Updated register A |  |  |  |  |  |  |  |  | 

## Slide 53: Bits & Registers
Clear bit(s) in register: (A &= ~B), long form: (A = A & ~B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Inverted value B | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0xDD
Updated register A |  |  |  |  |  |  |  |  | 
Toggle bit(s) in register: (A ^= B), long form: (A = A ^ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A |  |  |  |  |  |  |  |  | 
New value B |  |  |  |  |  |  |  |  | 
Updated register A |  |  |  |  |  |  |  |  | 

## Slide 54: Bits & Registers
Clear bit(s) in register: (A &= ~B), long form: (A = A & ~B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Inverted value B | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0xDD
Updated register A | x | x | 0 | x | x | x | 0 | x | 
Toggle bit(s) in register: (A ^= B), long form: (A = A ^ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A |  |  |  |  |  |  |  |  | 
New value B |  |  |  |  |  |  |  |  | 
Updated register A |  |  |  |  |  |  |  |  | 

## Slide 55: Bits & Registers
Clear bit(s) in register: (A &= ~B), long form: (A = A & ~B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Inverted value B | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0xDD
Updated register A | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0x85
Toggle bit(s) in register: (A ^= B), long form: (A = A ^ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A |  |  |  |  |  |  |  |  | 
New value B |  |  |  |  |  |  |  |  | 
Updated register A |  |  |  |  |  |  |  |  | 

## Slide 56: Bits & Registers
Clear bit(s) in register: (A &= ~B), long form: (A = A & ~B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Inverted value B | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0xDD
Updated register A | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0x85
Toggle bit(s) in register: (A ^= B), long form: (A = A ^ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | x | x | x | x | x | x | x | x | 
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A |  |  |  |  |  |  |  |  | 

## Slide 57: Bits & Registers
Clear bit(s) in register: (A &= ~B), long form: (A = A & ~B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Inverted value B | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0xDD
Updated register A | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0x85
Toggle bit(s) in register: (A ^= B), long form: (A = A ^ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | x | x | x | x | x | x | x | x | 
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A | x | x | ~x | x | x | x | ~x | x | 
If a bit in B is ‘1’, the corresponding bit in A will be inverted (toggled).
Notes: A ^= B: Where bit mask is 1, the updated register will change

## Slide 58: Bits & Registers
Clear bit(s) in register: (A &= ~B), long form: (A = A & ~B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Inverted value B | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0xDD
Updated register A | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 0x85
Toggle bit(s) in register: (A ^= B), long form: (A = A ^ B) |  |  |  |  |  |  |  |  | 
Operation | bit 7 | bit 6 | bit 5 | bit 4 | bit 3 | bit 2 | bit 1 | bit 0 | Hex
Register value A | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1 | 0xA5
New value B | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0x22
Updated register A | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 0x87
If a bit in B is ‘1’, the corresponding bit in A will be inverted (toggled).
Notes: A ^= B: Where bit mask is 1, the updated register will change

## Slide 59: Bit-fu 2nd Dan
Syntax | Long Form | Operation
A ¦= B | A = A ¦ B | A = Bitwise OR of A and B
A &= B | A = A & B | A = Bitwise AND of A and B
A ^= B | A = A ^ B | A = Bitwise XOR of A and B
A &= ~B | A = A & (~B) | A = Bitwise AND of A and NOT B
A += B | A = A + B | A = Add A and B
A -= B | A = A - B | A = Subtract B from A
A *= B | A = A * B | A = Multiply A with B
A /= B | A = A / B | A = Divide A with B
A >>= n | A = A >> n | A = Right shift A n bits
A <<= n | A = A << n | A = Left shift A n bits
A++ | A = A + 1 | A = Add 1 to A (Increment)
A-- | A = A - 1 | A = Subtract 1 from A (Decrement)

## Slide 60: Registers
C example
// Start out with pins PA2 and PA3 high
PORTA.OUT = (1 << PIN3_bp) | (1 << PIN2_bp);
// Set PA5 high without changing PA2 and PA3
PORTA.OUT |= (1 << PIN5_bp);
// Set PA2 low without changing PA5 and PA3
PORTA.OUT &= ~(1 << PIN2_bp);
Notes: Add actual values

## Slide 61: Registers
C example
// Start out with pins PA2 and PA3 high
PORTA.OUT = (1 << PIN3_bp) | (1 << PIN2_bp);
// Set PA5 high without changing PA2 and PA3
PORTA.OUT |= (1 << PIN5_bp);
// Set PA2 low without changing PA5 and PA3
PORTA.OUT &= ~(1 << PIN2_bp);
0b00001100
Notes: Add actual values

## Slide 62: Registers
C example
// Start out with pins PA2 and PA3 high
PORTA.OUT = (1 << PIN3_bp) | (1 << PIN2_bp);
// Set PA5 high without changing PA2 and PA3
PORTA.OUT |= (1 << PIN5_bp);
// Set PA2 low without changing PA5 and PA3
PORTA.OUT &= ~(1 << PIN2_bp);
0b00101100
Notes: Add actual values

## Slide 63: Registers
C example
// Start out with pins PA2 and PA3 high
PORTA.OUT = (1 << PIN3_bp) | (1 << PIN2_bp);
// Set PA5 high without changing PA2 and PA3
PORTA.OUT |= (1 << PIN5_bp);
// Set PA2 low without changing PA5 and PA3
PORTA.OUT &= ~(1 << PIN2_bp);
0b00101000
Notes: Add actual values

## Slide 64: Registers
Check if bit(s) are set
In C, everything except 0 is «True»
        if (PORTA.IN & (1 << PIN3_bp) ) {
        // PA3 is high, do something
        }
        if (PORTA.IN & (1 << PIN3_bp) != 0) {
        // PA3 is high, do something
        }

## Slide 65: Registers
Check if bit(s) are cleared
Can also be written as compare with 0
        if (!(PORTA.IN & (1 << PIN3_bp))) {
        // PA3 is low, do something
        }
        if (PORTA.IN & (1 << PIN3_bp) == 0) {
        // PA3 is low, do something
        }

## Slide 66: Registers
Store the current register state
Check if bit was set, may have changed
        uint8_t my_variable = PORTA.IN;
        if (my_variable & (1 << PIN3_bp)) {
        // PA3 was high, do something
        }

## Slide 67: ATmega4809 Curiosity Nano

## Slide 68: Curiosity Nano Adapter

## Slide 69: OLED1 Xplained Pro

## Slide 70: Hardware User Guide

## Slide 71: Hardware User Guide

## Slide 72: AVR I/O - Output
Controlled by the MCU
  0 == GND, 1 == VCC
  Example: LEDs
    «Active High» or «Active Low»
AVR Pin
GND
VCC
AVR Pin

## Slide 73: AVR I/O - Output
Controlled by the MCU
  Pin = 0 == GND
  Example: LEDs
    «Active High» or «Active Low»
AVR Pin = GND
GND
VCC
AVR Pin = GND
Pin = 0
0 V
3.3 V
No current
Current flow

## Slide 74: AVR I/O - Output
Controlled by the MCU
  Pin = 1 == VCC
  Example: LEDs
    «Active High» or «Active Low»
AVR Pin = VCC
GND
VCC
AVR Pin = VCC
Pin = 1
3.3 V
0 V
Current flow
No current

## Slide 75: AVR I/O - Output
Controlled by the MCU
  0 == GND, 1 == VCC
  Example: LEDs
    «Active High» or «Active Low»
AVR Pin
GND
VCC
AVR Pin

## Slide 76: AVR I/O - Input
Controlled externally
  Floating - Undefined state when not connected
  0 ~= GND, 1 ~= VCC
  The pin voltage needs to be «pulled» to 0 or 1
GND
AVR Pin = Floating
? V

## Slide 77: AVR I/O - Input
Controlled externally
  Floating - Undefined state when not connected
  0 ~= GND, 1 ~= VCC
  The pin voltage needs to be «pulled» to 0 or 1
GND
AVR Pin = GND
0 V

## Slide 78: AVR I/O - Input
Example: Switches
  Pull-up
GND
AVR Pin
VCC

## Slide 79: AVR I/O - Input
Example: Switches
  Pull-up
GND
AVR Pin = VCC
VCC
0 V, as pin voltage is pulled up
3.3 V

## Slide 80: AVR I/O - Input
Example: Switches
  Pull-up - Active Low
GND
AVR Pin = GND
VCC
3.3 V
0 V, as pin voltage is pulled down hard

## Slide 81: AVR I/O - Input
Example: Switches
  Pull-up - Active Low
GND
AVR Pin = GND
VCC
3.3 V, still trying to pull up,
current limited by resistor
0 V, as pin voltage is pulled down hard
no limitation on current

## Slide 82: AVR I/O - Input
Example: Switches
  Pull-down - Active High
  Same same, only inverted
VCC
GND
AVR Pin

## Slide 83: AVR I/O - Input
Example: Switches
  Pull-down - Active High
  Same same, only inverted
VCC
GND
AVR Pin

## Slide 84: Time to play!
https://omegav.no/avrkurs
OV people provide support
Microchip people support the support

## Slide 85: Time to play!
https://omegav.no/avrkurs
MPLAB X IDE: Open the .X folder
  Each task is a configuration in the project
Microchip Studio: Open the *.atsln file
  One project for each task

## Slide 86: Unexpected info!

## Slide 87: Bit-fu 3rd Dan
http://realtimecollisiondetection.net/blog/?p=78

## Slide 88
The three next slides are to be presented 1-2 hours into the hands-on tasks,
if we are confident the bitshifting has been understood..

## Slide 89: Some tips to simplify stuff
Egil will talk a bit more at 20:00

## Slide 90: Bitmasks again
In the header file:
How I would write it:
        #define PIN3_bp 3
        #define PIN3_bm (1 << PIN3_bp)
        PORTA.OUT = PIN3_bm;
        USART.CTRLB = USART_TXEN_bm;
        PORTA.PIN2CTRL = PORT_ISC_LEVEL_gc;

## Slide 91: Bitmasks again
In the header file:
How I would write it:
Named settings in header file:
(Not valid for ATmega328 and other old devices)
        #define PIN3_bp 3
        #define PIN3_bm 0x08
        PORTA.OUT = PIN3_bm;
        USART.CTRLB = USART_TXEN_bm;
        PORTA.PIN2CTRL = PORT_ISC_LEVEL_gc;
Notes: _bm vs _gc

## Slide 92: Making GPIO life easier
We have added PORT registers that does set, clear and toggling for you!
DO NOT USE |= OR &= OR ^= HERE
        PORTA.OUTSET = PIN3_bm;
        PORTA.OUTTGL = PIN7_bm;
        PORTA.OUTCLR = PIN3_bm;

## Slide 93: Correct Read-Modify-Write
The Control C register was configured like this:
We want to change reference from VDD to VREFA
Can be combined into one line
Or just reconfigure all the bitfields
ADC0.CTRLC = ADC_REFSEL_VDDREF_gc | ADC_PRESC_DIV128_gc;
ADC0.CTRLC &= ~ADC_REFSEL_gm;
ADC0.CTRLC |= ADC_REFSEL_VREFA_gc;
ADC0.CTRLC = (ADC0.CTRLC & ~ADC_REFSEL_gm) | ADC_REFSEL_VREFA_gc;
ADC0.CTRLC = ADC_REFSEL_VREFA_gc | ADC_PRESC_DIV128_gc;

## Slide 94: Correct Read-Modify-Write – Compiled
18e:e0 e0 ldi r30, 0x00 ; Address to ADC0 struct (Z-pointer low byte)
190:f6 e0 ldi r31, 0x06 ; Address to ADC0 struct (Z-pointer high byte)
ADC0.CTRLC &= ~ADC_REFSEL_gm;
196:82 81 ldd r24, Z+2 ; Load ADC0.CTRLC into r24 (byte 2 in ADC0 struct)
198:8f 7c andi r24, 0xCF ; r24 &= ~ADC_REFSEL_gm
19a:82 83 std Z+2, r24 ; Load r24 into ADC0.CTRLC
ADC0.CTRLC |= ADC_REFSEL_VREFA_gc;
19c:82 81 ldd r24, Z+2 ; Load ADC0.CTRLC into r24
19e:80 62 ori r24, 0x20 ; r24 |= ADC_REFSEL_VREFA_gc
1a0:82 83 std Z+2, r24 ; Load r24 into ADC0.CTRLC
ADC0.CTRLC = (ADC0.CTRLC & ~ADC_REFSEL_gm) | ADC_REFSEL_VREFA_gc;
1a2:82 81 ldd r24, Z+2 ; Load ADC0.CTRLC into r24
1a4:8f 7c andi r24, 0xCF ; r24 &= ~ADC_REFSEL_gm
1a6:80 62 ori r24, 0x20 ; r24 |= ADC_REFSEL_VREFA_gc
1a8:82 83 std Z+2, r24 ; Load r24 into ADC0.CTRLC
ADC0.CTRLC = ADC_REFSEL_VREFA_gc | ADC_PRESC_DIV128_gc;
1aa:86 e2 ldi r24, 0x26 ; Hex value of ADC_REFSEL_VREFA_gc | ADC_PRESC_DIV128_gc
1ac:82 83 std Z+2, r24 ; Load r24 into ADC0.CTRLC

## Slide 95: Thank You, Microchip leaves at 21:00 
Two hands in the air if you want merch in the mean time